## Slide 1: Two Wheel Self Balancing robot
Sidhant Chanana
Varun Jain

## Slide 2: Stabilization and Movement
1- We started out with using reinforcement learning algorithm PPO for both balancing and translation of the robot from its point of origin to target point
2- Due to low success rate even after high number of epochs we switched the approach
3- Now for stabilization we are using a PID controller which helps balance the robot upright based on the tilt angle values it gets
4- For translation of robot we are using PPO

## Slide 3: Balancing the Robot
1- We used PID logic to balance the robot. The tilt angle or the pitch helps us decide the amount of torque that is being translated to the wheels to keep the robot upright
2- The tilt angle is measured with respect to the vertical axis which is the y-axis in pybullet.
3- The differential torque on the wheels helps control the pitch of the robot to keep it upright by the movement of wheels

## Slide 4: Movement towards the Goal
1- The RL algorithm that we used is DQN Neural Network design
2- The states being recorded are:- The state vector looks like this [x_position, y_position, distance_to_target, angle_to_target]
3- The actions are:- torque values that are controlling the robot

## Slide 5: Reward Function Calculation
1- The reward function is as follows:-
Distance to target is minimized
Reward= -(distance_to_target)-0.1*abs(angle_to_target)
2- The Q-value updates as follows:-
Loss is calculated using MSE between target Q and current Q